## Slide 1: Side Channel Attacks Analysis for Secure ISA and Architecture
Presentation
Abishek Barve
Richmond Johnson David Bhaskaran
Tanushree Tanushree

## Slide 2: Aim and Motivation – shortfalls in current mapping techniques in many-core mapping algorithms
Novel algorithms for application mapping in many core architectures tend to focus on improving performance and efficiency by assigning specific functionalities to localized nodal clusters
Although it may achieve its designated goals in terms of speed, one cannot deny that it leverages predictable patterns of the system behavior, and this when exploited by an external/internal attacker can lead to a blueprint of the internal mapping architecture being exposed
The attacker (depending on his type – either a memory or cache or even a processor blocking attacker) may then choose to attack a particular cluster set
For example, there may be a particular cluster dedicated to performing only memory (either L2, L3 or Main Memory) transactions and therefore accessing the cache contents of this cluster may expose the data exchanges being performed by the system as a whole
In another case, even if the memory access is evenly distributed across the clusters, an attacker manages to read the cache contents is able to know what data is being processed/exchanged by each individual clusters

## Slide 3: Aim and Motivation – shortfalls in cache vulnerabilities in multi-nodal clusters
Therefore from the above points, it can be definitively concluded that an insight into the cache is equivalent to exposing the system behavior as a whole up to the level of instruction level data exchanges
Even if the mapping algorithms are perfect such that functionalities are distributed evenly across clusters, an attack on the cache still exposes the system
It becomes necessary to protect the cache contents as it is the entry point for a number of attacks
In this project, we explore the cache related attacks in multi-nodal multi core systems and make best efforts to provide safety against such attacks

## Slide 4: Algorithm – Attacker Emulation
Step 1. Fill entire L2 and L1 cache with cache blocks using attacker program and note access time of each individual cache line
Step 2. Flush the entire L2 and L1 cache using clflush instruction
Step 3. Run Victim program and fill cache blocks used by victim in L2 cache
Step 4. Again run Attacker program to load cache blocks in L2 cache and note down access time of each individual cache line
Step 5. Is access time of all blocks same?
Step 6. Blocks with less access time as compared to other are used by victim program
Step 6. No cache blocks were accessed by victim program
Yes
No

## Slide 5: Cache Model Algorithm Explanation
x | x+y | x+y | x+y
x+y | x | x+y | x+y
x | x+y | x+y | x+y
x+y | x+y | x+y | x+y
x+y | x+y | x+y | x+y
x+y | x+y | x+y | x+y
x | 
 | x
x | 
Victim Program L1(From LLVM)
Attacker Program L1
Shared L2 Cache
x -> access time for a block which is present in L2 cache
Y -> access time of block not present in L2 cache and needs to be accessed from main memory
Main Memory

## Slide 6: Program Flow
Victim_trace generated from LLVM
Attacker_trace
Run Attacker trace on Cache Model
Note Old Access time for each Block
Flush L2 Cache
Run Victim trace on Cache Model
Again Run Attacker trace on Cache Model
Note New Access time for each Block
Save Block Address , Old Access time and New Access time in Result file and analyze the result in graphs
Steps to find access time in Cache
Search Block in L1 -> If found, already present in L2
If not found in L1 -> Search Block in L2 cache
If found in L2 -> access time will be equal L1 miss latency
If not found in L2 -> access time will be equal to L2 miss latency

## Slide 7: Implemented Code
Pseudocode to search a cache block in L1 and L2 cache by attacker and calculate the time taken to search initially
i=0
While (line in attacker file):
time_start = time()
search = L1_attacker.search(line)
If(!search):
search_l2 = L2.search(line)
If(!search_l2):
L2.install(line)
L1_attacker.install(line)
time_end = time()
time_block_old[i] = time_start - time_end
i++
Pseudocode to search a cache block in L1 and L2 cache by victim
While (line in victim file):
search = L1_victim.search(line)
If(!search):
search_l2 = L2.search(line)
If(!search_l2):
L2.install(line)
L1_victim.install(line)

## Slide 8: Implemented Code
Pseudocode to search a cache block in L1 and L2 cache by attacker and calculate the time taken to search second time
i=0
While (line in attacker file):
time_start = time()
search = L1_attacker.search(line)
If(!search):
search_l2 = L2.search(line)
If(!search_l2):
L2.install(line)
L1_attacker.install(line)
time_end = time()
time_block_new[i] = time_start - time_end
i++
Compare time-analysis to find if cache block accessed by Victim
for(i in time_block_new):
if(time_block_new[i]!=time_block_old[i]):
printf "Accessed block i by victim"
Else:
Printf "not accessed"

## Slide 9: What is memory footprint ?
The addresses accessed by a particular program during its execution
Addresses in this context corresponds to the variables used by the program
Due to principle of locality, many programs have their variables placed nearby in their stack frames and by extension, in memory (both main memory and caches)
addresses
# of
accesses
main

## Slide 10: Why is this vulnerable?
Just like in a game of battleships, if an attacker finds one relevant address of the victim program, he can deduce the other addresses because it is definitely going to be the nearby ones
addresses
# of
accesses
main

## Slide 11: Naïve solution
So, to tackle this, can we distribute the variables in random inside the address space ?
Then that would come at a terrible performance
In fact, it would beat the purpose of high speed caches and would violate a ton of Operating system concepts and program mapping into memory
addresses
# of
accesses

## Slide 12: Improvised solution
What if we give an impression that the victim program is working on a ton of variables, when in fact it is working on a few
Then the attacker has to browse through many variables and he will never be able to settle in on the exact variables
addresses
# of
accesses

## Slide 13: Improvised solution
Lets assume that we present an illusion that we are working with 100 variables, when in actuality we are working with only 10
In the original (vulnerable) scenario, the attacker will definitely know that 10 variables are being used by the victim and he will always find those 10 variables – Probability of successful attack = 100%
In the improvised scenario, now the attacker has to guess among 100 variables !
Even if he knew that the victim uses only 10 critical variables, now he has to guess 10/100 locations Probability of successful attack ~ 0 to 100%
addresses
# of
accesses

## Slide 14: Inspiration for the solution
This technique is already used in Digital Communication Systems as Frequency Hopped Spread Spectrum Modulation – from World War 2
Instead of settling at one critical frequency (fc) which is easily deducible by an attacker, what if the sender and receiver are tuned to send/receive from a range of frequencies fc1 to fc2
Then the attacker will never be able to settle in on the frequency at which they communicate as it is bound to change after a time slice
Likewise, by not allowing the attacker to settle in on one memory address, we are ensuring safety to some degree
Simple Basis : If you cannot convince them, then confuse them
addresses
# of
accesses
Frequency
Gain
Frequency Hopped Spread Spectrum modulation
fc1
fc2
Security through address space widening

## Slide 15: How to achieve this ?
Compiler Based Solutions
  Include Dummy Variables
    What if we can provide this as a background solution without asking the user to include 100’s of fake variables ?
  Break a long iterator or array into interleaved sections
    Without considerable reduction in performance
  A combination of solutions to produce a unified framework ?
  Etc..
Hardware Based Solutions
  What if one thread is dedicated to loading dummy addresses
    without loss in performance
    Use of a mathematical function
  Opens up an entire arena of Hardware based randomization

## Slide 16: Our Approach
We decided to go for the dummy variable approach as proof of concept
Concerns
  Dummy Variables must not blow up the stack
  Dummy Variables must not interfere with regular working of program
  Dummy Variables must be included in background
  Dummy variables must not cause measurable loss in performance
  Must be a solution to be applicable to all languages and architectures
  The security framework must be a plugin and should provide seamless integration to any existing compilation framework
These are the necessary components to our PoC
  An LLVM toolchain and clang based environment that would convert any front-end program into an IR representation
  A script that converts the IR to assembly format
  A script that analyzes the assembly file to identify suitable spots and include dummy variables
  A script that gets the objdump and populates the necessary inputs for a cache emulator that runs attacker and victim programs
  A script that provides the output graph solution for visual representation
  To note: the security feature (including dummy vars) is a configurable feature that can be turned ON/OFF

## Slide 17: Our Approach
.c file
.ll file
.S file
exe file
objdump
Victim trace file
Cache Emulator
Pre – compiled Attacker and its trace files
Emulation of CONTECH Tool
Output .csv files
Graph Template
Output Graphs
Identify all variables in the address space
Include Dummy Variables
Modified .s file
If secure execution is turned ON

## Slide 18: Result From Cache Algorithm
Results when secure algorithm off
Results when secure algorithm on
With Security, attacker is able to find 100% of the actual victim used addresses for a program
With Security, attacker is able to find 66.66% of the actual victim used addresses for a program

## Slide 19: Future Scope
As new approaches are discovered, all the solutions – both compiler based and hardware based can be compiled into a framework
This opens a new arena in Hardware Security
  Hardware Based Hardware Security
  Software Based Hardware Security
Collaboration from a number of Engineers in the
  Computer Architecture Division
  Compilers Division
  Operating Systems Division
  Hardware Division
  System Software Division
  Firmware Division
  To Provide a unified solution that can tackle Hardware Security as Side Channel Attacks – SCA are emerging threats !

## Slide 20: Thank You